PipeLine Separates™

No. 1571-TS TyreSwing™

TyreSwing shall be PipeLine® model No. 1571-TS in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A. Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Swing shall consist of four posts, beam, two arches, tire, chain, and swivel.  Beam, posts, and arches shall be 4-1/2" (o.d.) schedule 40 steel pipe.

Tire shall be manufactured from medium density polyethylene, black in color, and include built in eye bolts to accept attachment hardware.  Tire shall be of a closed design so as not to collect water.  Rubber tires or similar open styles shall not be accepted.

Swivel and seat shall attach to hardened chain.  Swivel mounting brackets shall be 1/4 inch thick mild steel plate.  Tire shall attach to chain with double opening shackles and tamper-resistant hardware.

2.  CONSTRUCTION

Swivel shall include thrust bearing for 360( rotation plus a universal joint for 160( lateral range of motion.  The universal joint shall be covered with a close-fitting, flexible, neoprene rubber boot, and the swivel shall be equipped with two zerk fittings to receive regular lubrication by playground equipment maintenance personnel.

3.  FINISH

Posts, beam, and arches shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Swing mounting brackets shall be finished standard black.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Swing chain and assembly hardware shall be galvanized.