TimberForm Separates™

# No. 1600 SpringPad™

SpringPad shall be TimberForm® model No. 1600 in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

SpringPad shall consist of six deck members, spring assembly, and assembly hardware.  Decking shall be 3 x 8 Playground Equipment Grade free-of-heart-center (F.O.H.C.) Douglas fir timbers, selected by the equipment manufacturer for strength, durability, and appearance.  Spring assembly shall consist of four 9" high tension automotive-type coil springs and 1/4" thick steel top and bottom plates.

2.  CONSTRUCTION

Timber decking shall be free of wane with all edges eased (rounded) to a 1/4 inch radius.  Once assembled, deck members shall form a 3'-10" x 3'-10" square pad.  Springs shall be permanently welded to the plates to provide spring action.

3.  FINISH

Timber materials shall pressure treated with a non-toxic child safe preservative after all fabrication is completed.  Preservatives containing arsenic, pentachlorophenol, creosote or similar toxic chemicals as their active ingredient shall not be used.

Spring assembly shall be finished black with CASPAX-™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.