# TimberForm/PipeLine Separates™

1602-01-00 Stepping Pad

Stepping Pad shall be TimberForm®/PipeLine® model No. 1602-01-00 in the height and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Top of pad shall be constructed of 3/16" thick mild steel plate and circular 1-5/8" (o.d.) schedule 40 steel pipe.  Four 3/16" thick mild steel plate gussets shall reinforce the pad and fasten it to a 2-3/8" (o.d.) schedule 40 mild steel seamless pipe post.

2.  CONSTRUCTION

Pad, gussets, and post shall be permanently welded into a one-piece unit.  Embedded portion of Stepping Pad shall include two thru holes to receive No. 4 re-bar supplied by installing contractor.

3.  FINISH

After fabrication, entire Stepping Pad shall receive ultra-violet stabilized thermoplastic coating applied by the electrostatic process to the pre-heated substrate to a thickness of approximately 30 mils then allowed to cure before handling.  Final Durometer (hardness) shall be 52 on the D Shore scale in accordance with ASTM D 2240.