# PipeLine Separates™

Model No. 1630-2-21-PL KidMixer™

KidMixer shall be PipeLine® model No. 1630-2-21-PL in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, Oregon 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

KidMixer shall consist of platform assembly and base assembly with pole.

Platform assembly shall be fabricated from 11 ga. slotted steel sheet and have a permanently welded outside ring constructed of 1-5/16" (o.d.) schedule 40 steel pipe.  Base assembly shall include a hub with automotive wheel bearings and a curved pole fabricated from 1-5/16" (o.d.) schedule 40 steel pipe with a 1” dia. curved steel rod insert.

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3. METAL FINISH

All metal parts other than those galvanized or stainless steel shall be finished with CASPAX-7™, a colorful, tough, opaque, exterior use powder coating.  Liquid, epoxy, or lead-containing powder coatings are not acceptable.