# PipeLine Separates™

Model No. 1630-6-12-PL WhirlAround™

WhirlAround shall be PipeLine® model No. 1630-6-12-PL in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, Oregon 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

WhirlAround shall consist of a top assembly and base with hub assembly.

Top assembly shall have a hexagonal shaped outside grip bar formed from curved 1-5/16" (o.d.)schedule 40 steel pipe.  Spokes formed from curved 1-5/16" (o.d.) schedule 40 steel pipe shall radiate from outside grip bar and be welded to a 4-1/2" (o.d.) schedule 40 steel pipe post section which shall be fitted with a cast aluminum hemi-dome end cap.  Additional curved 1-5/16" (o.d.) schedule 40 steel pipe shall be welded to the spokes and the center post for added rigidity. Top assembly shall connect to hub by a circular 3/8” steel plate flange with eight 7/16” square holes and 3/8” carriage bolts and hardware.

Hub assembly shall consist of a 3/8” bearing flange welded to a mitered 4-1/2" (o.d.) schedule 40 steel pipe post section fitted with two long life roller bearings.  Mitered end of hub assembly shall be permanently welded to mitered 4-1/2" (o.d.) schedule 40 steel pipe post.

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3. METAL FINISH

All metal parts other than those galvanized or stainless steel shall be finished with CASPAX-7™, a colorful, tough, opaque, exterior use powder coating.  Liquid, epoxy, or lead-containing powder coatings are not acceptable.