# PipeLine Separates™

### No. 1693-11-PL Overhead Arch Ladder with Handrails

Overhead Arch Ladder with Handrails shall be PipeLine® model No. 1693-11-PL in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Overhead Arch Ladder with Handrails shall consist of four embedded support posts and one arch ladder assembly.

Support posts shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32". Thin wall tubing is not acceptable.

Arch Ladder Assembly shall be two formed 4-1/2" (o.d.) schedule 40 steel pipe rails with 13 each evenly spaced 1-5/16" (o.d.) schedule 40 steel rungs and formed 1-5/16” (o.d.) schedule 40 steel pipe handrails with equally spaced balusters, all permanently welded in place to form a one-piece assembly.

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.