# TimberForm & PipeLine Separates™

### No. 1695 Parallel Bars

Parallel Bars shall be TimberForm®/PipeLine® model No. 1695 in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Parallel Bars shall consist of two handrails.

Handrails shall be curved 1-7/8” (o.d.) schedule 40 steel pipes, 8’-2” long, 3’-6” high, parallel and mounted 2’-5” on center.

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.