# PipeLine Separates™

# No. 1959-7-27-PL Tube Chute, ‘S’-Curved, Vertical Safety Climber™

Tube Chute, ‘S’-Curved, Vertical Safety Climber shall be PipeLine® model No. 1959-7-27-PL, seven feet high, in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Tube Chute with Vertical Safety Climber shall consist of support posts, entrance platform, vertical safety climber, and a plastic tube chute, plus attachment hardware.

Support posts shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32". Thin wall tubing is not acceptable.

Entrance platform shall be a one-piece welded assembly that consists of a diamond plate steel deck, two sleeved post extensions, safety barrier walls, and attachment hardware.  The diamond plate steel deck shall be 1/4" thick and formed to have 2-3/4" reinforced edges.  It shall be supplied in the length and width to properly fit the attaching accessory.  The sleeved post extensions shall be 4-1/2" o.d. schedule 40 steel pipe with a minimum wall thickness of 7/32".  The post extensions shall be welded to the notched edges of the platform and include sleeves to allow for attachment to the structure support posts.

The safety barrier walls shall consist of 1-5/16" (o.d.) schedule 40 curved steel pipe frames with 5/8" diameter steel rod pickets.  The top of the barrier walls shall extend 38" above the platform surface and include the required safety bars to aid in channeling the users of the structure to a safe, seated position as applicable.

Vertical Safety Climber shall consist of vertical safety climber assembly, two side enclosure assemblies, and attachment hardware.  Vertical safety climber assembly shall consist of 1-5/16" (o.d.) rungs and 1-11/16" (o.d.) schedule 40 steel pipe frame, and vertical pole, assembled into a one-piece unit.  The completed climber shall measure 1'-6" wide and meet the specified height requirements.

Side enclosure assembly shall consist of a one-piece enclosure.  Enclosure shall be 1-5/16" (o.d.)  schedule 40 steel pipe permanently welded to one 5/8" diameter solid steel baluster.

Plastic Tube Chute shall consist of one panel with hole, tunnel sections, one support bracket, one support post and attachment hardware.  Tunnel sections shall be polyethylene formed in 24" diameter units and tan or yellow in color.  Wall thickness shall average .375 inches.  Thinner wall thickness is not acceptable.  Interior surfaces shall be smooth and the exterior shall have a textured finish.  Segments shall be smoothly fitting and fastened with integral nuts.

Page 1 of 2

Page 2 of 2

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3.  FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.