# TimberForm Separates™

### No. 3870-4 Tanderm Spring Rider See-Saw

Tandem Spring Rider See-Saw shall be TimberForm® model No. 3870-4 in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

See-Saw shall consist of beam, four handles, four seats, and two springs. Standard mounting shall be -E embedment (permanent).  Optional: -P pedestal (fixed surface) mount.

Seat shall be manufactured from 3/4" thick tri-layered high-density compression molded polyethylene. Exposed panel edges shall be eased (rounded) with 3/16" radius.  Polyethylene shall be formulated for optimum U.V. stability and color retention.

Springs shall be manufactured from 25/32" (20 mm) thick wire.  Spring plates shall be a deep drawn product contoured to match the spring and form a single unit with finger-pinching protection.  The springs shall be guaranteed by the manufacturer against breakage for five years.

Steel post and beam shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32".  Exposed ends of the beam shall be fitted with a cast aluminum (384 alloy) hemi-dome end cap permanently double riveted in place.  Handles shall be 1-5/16" (o.d.) schedule 40 steel pipe permanently welded to the beam.

Embedment (-E) mount see-saw shall include three 1-5/16" (o.d.) schedule 40 steel pipe legs which embed in concrete.  Pedestal (-P) mount see-saw shall have three 3/4" diameter holes to receive anchor bolts (supplied by installing contractor).

2. CONSTRUCTION

Ends of springs shall be closed and ground smooth prior to finishing.  Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

All steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.  Spring shall be zinc phosphate coated prior to powder-coating.