# No. 4500-101 TimberCraft® PlayFrame™

PlayFrame shall be TimberCraft® model No. 4500-101 as manufactured by Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

PlayFrame shall consist of eight natural tapered wood poles 15’ long with 8” butt diameter, steel frame, cable rope, eight steel surface mounting brackets, and assembly hardware.

Mounting brackets shall be fabricated from 1/4” thick steel plate in accordance with ASTM A-36.

2.  CONSTRUCTION

Poles shall be hand-peeled of bark and sanded.  Poles that have been machine peeled or that include bark will not be accepted. To effectively receive pressure preservative treatment, all fabrication, including sawing, notching, and drilling must be completed prior to preservative treatment.

Frame welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3.  FINISH

Timber poles shall be pressure treated with a non-toxic child safe preservative after all fabrication is completed.  Preservatives containing arsenic, pentachlorophenol, creosote or similar toxic chemicals as their active ingredient shall not be used.

Frame and mounting brackets shall be finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

4.  INSTALLATION INSTRUCTIONS AND AIDS

To guide installation, each TimberCraft structure shall be accompanied by bills of materials and an erection plan view drawing to be furnished prior to or with the delivery of the play structure.  To facilitate assembly, each part shall be indelibly stenciled with an easily-read identification number keyed to the bills of material and erection drawings.  All components shall be shipped unitized, protectively wrapped, banded for mechanical handling and ready for assembly.