# TimberForm Separates™

# No. 1561-TS TyreSwing™

TyreSwing shall be TimberForm® model No. 1561-TS in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Swing shall consist of four posts, beam, tire, chain, and swivel.  Beam shall be 6 x 8 and posts shall be 6 x 6 Playground Equipment Grade free-of-heart-center (F.O.H.C.) Douglas fir timbers, selected by the equipment manufacturer for strength, durability, and appearance.

Tire shall be manufactured from medium density polyethylene, black in color, and include built in eye bolts to accept attachment hardware.  Tire shall be of a closed design so as not to collect water.  Rubber tires or similar open styles shall not be accepted.

Swivel and seat shall attach to hardened chain.  Swivel mounting brackets shall be 1/4 inch thick mild steel plate.  Tire shall attach to chain with double opening shackles and tamper-resistant hardware.

2.  CONSTRUCTION

Timber posts and beam shall be free of wane with all edges eased (rounded) to a 1/4 inch radius.  Post tops shall be chamfer-sawn 45 degrees to promote rain water drainage.  Each chain shall swing freely from a UHMW bushing for maximum wear resistance without requiring periodic maintenance. .  Bronze bearings shall not be accepted.

Swivel shall include thrust bearing for 360( rotation plus a universal joint for 160( lateral range of motion.  The universal joint shall be covered with a close-fitting, flexible, neoprene rubber boot, and the swivel shall be equipped with two zerk fittings to receive regular lubrication by playground equipment maintenance personnel.

3.  FINISH

Timber materials shall pressure treated with a non-toxic child safe preservative after all fabrication is completed.  Preservatives containing arsenic, pentachlorophenol, creosote or similar toxic chemicals as their active ingredient shall not be used.

Steel swing brackets shall be finished black with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Swing chain and assembly hardware shall be galvanized.