# PipeLine Separates™

# No. 1573-4 Double Belt / Double Tot Swing

Double Belt/Double Tot Swing shall be PipeLine® model No. 1573-4 in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Swing shall consist of six posts, two beams with integrally mounted hangers, two belt swing seats, two tot swing seats and chain.  Beams, posts, and arches shall be 4-1/2" (o.d.) schedule 40 steel pipe.

Belt and tot seats shall be tan rubber and fitted with concealed steel reinforcing straps.  Two loops shall be permanently riveted to each seat and attach to hardened chain.

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Each chain shall swing freely from a UHMW bushing for maximum wear resistance without requiring periodic maintenance.  Bronze bearings shall not be accepted.

3.  FINISH

Posts, beam, and arches shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Swing pivots shall be finished black.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Swing chain and assembly hardware shall be galvanized.