# TimberForm Separates™

No. 1628-12-01 Timber Balance Beam

Timber Balance Beam shall be TimberForm® model No. 1628-12-01 in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Timber Balance Beam shall consist of balance beam with three support legs.

Support legs shall be 1-7/8” (o.d.) schedule 40 steel pipe.  Balance Beam shall be 4 x 6 Playground Equipment Grade free-of-heart-center (F.O.H.C.) Douglas fir timber, selected by the equipment manufacturer for strength, durability, and appearance.

2.  CONSTRUCTION

Timber beam shall be free of wane with all edges eased (rounded) to a 1/4 inch radius.

3.  FINISH

Timber beam shall be pressure treated with a non-toxic child safe preservative after all fabrication is completed.  Preservatives containing arsenic, pentachlorophenol, creosote or similar toxic chemicals as their active ingredient shall not be used.

Support posts shall be finished black with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.