# PipeLine Separates™

Model No. 1630-1-20-PL Sloped Spinner

Sloped Spinner shall be PipeLine® model No. 1630-1-20-PL in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, Oregon 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1.  MATERIALS

Seat Spinner shall consist of top assembly and base with hub assembly.

Top assembly shall consist of one seat ring and a slotted steel platform.  Ring shall be constructed of 1-5/16" (o.d.) schedule 40 steel pipe permanently welded to the 3/16” steel plate platform.  Final assembly shall be one-piece for rigidity.

Base with hub assembly shall be 3-1/2” (o.d.) schedule 40 steel pipe fitted with two long life roller bearings.  Bearings shall be readily serviceable after installation.

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3. METAL FINISH

All metal parts other than those galvanized or stainless steel shall be finished with CASPAX-7™, a colorful, tough, opaque, exterior use powder coating.  Liquid, epoxy, or lead-containing powder coatings are not acceptable.