# PipeLine Separates™

### No. 1648-6-22-PL Double Arch Net Climber

Double Arch Net Climber shall be PipeLine® model No. 1648-6-22-PL in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Double Arch Net Climber shall consist of four curved beam assemblies, two arch net climber assemblies, one intermediate beam and two base brackets.

Curved beam assemblies shall be formed 4-1/2" (o.d.) schedule 40 steel pipes joined together at intermediate beam by tabs and inserts.  Intermediate beam shall be 4-1/2" (o.d.) schedule 40 steel pipe.

Arch net climber assemblies shall consist of hardened and plastisol-coated chain formed into a 12" grid with all intersections permanently joined.  Ordinary proof coil chain is not permitted.  Assemblies shall attach to pad-eyes permanently welded to beams with 5/16” galvanized quick links.

The final assembly shall form a 180-degree arc with an overall length of 19’-4” and height of 6 ft.

Base brackets shall be ¼” steel plate, each with four 9/16” diameter holes for anchoring bolts (by others).

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.