# PipeLine Separates™

### No. 1670-02-PL Single Arch Loop Climber

Single Arch Loop Climber shall be PipeLine® model No. 1670-02-PL in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Single Arch Loop Climber shall consist of climber assembly and two base brackets.

Climber assembly shall be two formed 4-1/2" (o.d.) schedule 40 steel pipe rails and 22 1-5/16" o.d. formed schedule 40 steel pipe loops which are evenly-spaced and permanently welded in place to form a one-piece assembly.  The one-piece assembly shall form a 180-degree arc with an overall length of 19’-6” and height of 6 ft.

Base brackets shall be ¼” steel plate, each with four 9/16” diameter holes for anchoring bolts (by others).

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.