# TimberForm & PipeLine Separates™

### No. 1693 Overhead Arch Ladder

Overhead Arch Ladder shall be TimberForm®/PipeLine® model No. 1693 in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Overhead Arch Ladder shall consist of ladder assembly and two base brackets.

Ladder assembly shall consist of 14 equally-spaced 1-5/16" (o.d.) schedule 40 steel pipe rungs permanently welded to 1-3/4" (o.d.) schedule 40 side rails.  Easily vandalized plastic and/or friction fit end caps are not permitted.  The one-piece assembly shall form a 180-degree arc.

Base brackets shall be ¼” steel plate, each with three 9/16” diameter holes for anchoring bolts (by others).

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.