# PipeLine Separates™

# No. 1940-6-24-PL Slide Chute, Stainless Steel with 6” Rails,

# Vertical Safety Climber

Slide Chute, Stainless Steel with 6” Rails, Vertical Safety Climber shall be PipeLine® model No. 1940-6-24-PL, six feet high, in the color finish and quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

- MATERIALS

Slide Chute, 6” Rails with Stairway with Baluster Handrails shall consist of support posts, entrance platform, stairway with handrails, and a Stainless Steel Slide Chute, plus attachment hardware.

Support posts shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32". Thin wall tubing is not acceptable.

Entrance platform shall be a one-piece welded assembly that consists of a diamond plate steel deck, two sleeved post extensions, safety barrier walls, and attachment hardware.  The diamond plate steel deck shall be 1/4" thick and formed to have 2-3/4" reinforced edges.  It shall be supplied in the length and width to properly fit the attaching accessory.  The sleeved post extensions shall be 4-1/2" o.d. schedule 40 steel pipe with a minimum wall thickness of 7/32".  The post extensions shall be welded to the notched edges of the platform and include sleeves to allow for attachment to the structure support posts.

The safety barrier walls shall consist of 1-5/16" (o.d.) schedule 40 curved steel pipe frames with 5/8" diameter steel rod pickets.  The top of the barrier walls shall extend 38" above the platform surface and include the required safety bars to aid in channeling the users of the structure to a safe, seated position as applicable.

Vertical Safety Climber shall consist of vertical safety climber assembly, two side enclosure assemblies, and attachment hardware.  Vertical safety climber assembly shall consist of 1-5/16" (o.d.) rungs and 1-11/16" (o.d.) schedule 40 steel pipe frame, and vertical pole, assembled into a one-piece unit.  The completed climber shall measure 1'-6" wide and meet the specified height requirements.

Side enclosure assembly shall consist of a one-piece enclosure.  Enclosure shall be 1-5/16" (o.d.)  schedule 40 steel pipe permanently welded to one 5/8" diameter solid steel baluster.

Page 1 of 2

Page 2 of 2

Slide Chute stainless steel bedway assembly shall consist of a 18" wide single sheet of 16-gauge T430 bright annealed stainless steel, side rails and safety handrails, and shall include no laps or seams.  It shall be permanently attached to the side rails with "monobolts", and shall be reinforced from underneath by 16-gauge galvanized steel battens spaced no further than 4" on center.  Each side rail shall be aluminum "D" rail, shall extend 6" above the slide bedway, and have ends closed with the end caps permanently riveted in place.  Each side rail shall incorporate safety rails at the top to provide a hand hold for the players and help channel them into a safe, seated, sliding position.  Front pipe brace assembly shall include 1" Schedule 40 galvanized steel tube.  Chute shall slope approximately 30 degrees when properly installed.  In the exit area (bottom), side rails and assembly shall be curved to parallel grade as closely as possible, thereby slowing the player for safe discharge.

2.  CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3.  FINISH

Metal components, other than those galvanized or stainless steel, shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.