# PipeLine Separates™

### No. 1993-12-00-PL Ring Beam

Ring Beam shall be PipeLine® model No. 1993-12-00-PL in the quantity shown on the bill of materials or the project drawings.  Colors shall be the manufacturer's standard.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Ste. 310, Portland, OR 97201-5293 U.S.A.  Phone 503/223-1157.

GENERAL

All fabrication shall take place in an enclosed factory environment by personnel experienced in the manufacture of children's play apparatus.

1. MATERIALS

Ring Beam shall consist of four posts, two end arch caps, one beam with integrally mounted hangers and seven ring assemblies.

Posts, arch caps and beam shall be 4-1/2" (o.d.) schedule 40 steel pipe with a minimum wall thickness of 7/32". Thin wall tubing is not acceptable.

Rings shall be triangular and cast aluminum.  Rings shall swing freely from a UHMW bushing for maximum wear resistance without requiring periodic maintenance.

2. CONSTRUCTION

Welds shall be smooth and continuous with no gaps or pinholes.  Final product shall be free of weld spatters and burrs.

3. FINISH

All metal parts shall be color finished with CASPAX-7™, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.